## Slide 1
Program counter
ROM
16 bit address
Reg 0
Reg 1
Reg 2
Reg 3
Reg 4
Reg 5
Reg 6
Reg 7
Reg 8
Reg 9
Reg10
Reg 11
Reg 12
Reg 13
Reg 14
Reg 15
Reg SP
16 bit data bus
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
*
Instruction Decode and Control
16 bit instruction
*
ALU In A Latch
ALU In B Latch
*
*
ALU
*
RAM Address Latch
RAM
16 bit address
*
*
Control signals are shown with “*”
Only the “Instruction Decode and Control” block writes these signals
Each Reg (including SP), Program Counter, and RAM has 3 control modes:
  Read from data bus
  Write to data bus
  Do nothing (output is high impedance tri-state)
RAM Address Latch and ALU In A/B have 2 control modes:
  Read from data bus
  Do nothing
ALU internal operation has N control modes
ALU output has 2 control modes:
  Write to data bus
  Do nothing (output is high impedance tri-state)
There may be 0 or 1 blocks writing to the
data bus at any one time.
There must never be more than one block
trying to write to the data bus at the same time.

## Slide 2
IS (Instruction sequencer) Page 1: Controlling writing to data bus
Needs to be able to select 0, or 1 of N, blocks to output on data bus.
There are 21 blocks that are capable of outputting to the data bus:
16 general purpose registers
SP (Stack Pointer)
PC (Program counter)
IS (Instruction sequencer) part of “Instruction Decode and Control) e.g. Load immediate
RAM
ALO (ALU Output)
It will need 5 bits (value 0..31) to specify which block should output on the data bus
Values 0..15 can be used for general purpose registers
Value 16 for SP, etc up to value 20 for ALU output
Values 21..30 are spare for now
Value 31 means no block should output on the data bus
Converting 5 bits to 32 individual control lines can be implemented with a demultiplexer e.g. Using https://eajournals.org/ijeees/wp-content/uploads/sites/53/2023/12/5-Line-to-32-Line.pdf

## Slide 3
IS (Instruction sequencer) Page 2: Controlling what reads from the data bus
Needs to be able to select 0, or 1 of N, blocks to read from data bus.
There are 22 Blocks that are capable of reading from the data bus
16 general purpose registers
SP (Stack Pointer)
PC (Program counter)
RAL (RAM Address Latch)
RAM
ALA (ALU In A Latch)
ALB (ALU In B Latch)
TBD may be a special mode for initialisation where IS puts zero on data bus and all blocks are filled with zero. As a minimum PC must be initialised, probably to zero, before CPU can start fetching instructions. Maybe there will be a hardware feature to automatically zero all registers and latches on power up.
See previous slide for note about 5 bit to 32 bit demultiplexer. There will need to be 2 such demultiplexers, one for write and one for read.

## Slide 4
IS (Instruction sequencer) Page 3: ROM Solution
From the previous 2 slides we need a 10 bit ROM word to control what writes to, and what reads from, the data bus.
The following tbds don’t affect the principle of a ROM sequencer, they are details that we don’t need to consider at this stage.
We may need additional bits for <tbd>?
  Inc PC (would be much slower if had to use ALU for this)
  Inc/Dec SP ( ditto )
  ALU function control other than input latches and output enable
  Something else?
We may be able to use bits directly from the op code to reduce ROM word size <tbd>?
The number of ROM words we need per CPU instruction depends on the number of steps in the instruction processing sequence.
For now, lets just assume that the maximum number of steps (NOS) is 16 <tbd>?
We will always choose a power of 2, so if 16 isn’t enough, we will use 32, or 64 etc
See next slide for ROM layout.

## Slide 5
IS (Instruction sequencer) Page 4: ROM Layout (NOS = 16)
Data = Sequence for instruction number 0
Data = Sequence for instruction number 1
Address
0
15
16
31
Data = Sequence for instruction number 2
32
47
... Etc ...
48
TBD how to map actual instructions on to an “Instruction number” for the ROM
E.g. CPY Ra, Rb could be 256 different instructions, or just 1 (latter seems more sensible)
TBD every instruction has to fetch instruction from ROM and store it in the IS block
Would that be part of every instruction in ROM or implemented in decidate hardware.

## Slide 6
IS (Instruction sequencer) Page 5: ROM Address Control (NOS = 16)
Let’s assume there are 64 different instruction numbers (NOI)
The actual number is tbd, 64 is chosen just as an example here
The lower N address bits (for NOS=16) A0..A3 select the step in the sequence
The next M address bits (for NOI=128) A4..A9 select the instruction number
A9 | A8 | A7 | A6 | A5 | A4 | A3 | A2 | A1 | A0
The blue bits will be set by the IS when the instruction has been decoded
So tbd – instruction 0 is special and always used to just fetch the instruction?
The green bits will be generated by a counter to go through the sequence of steps for
this instruction.
IS will set the counter for A3 to A0 to zero at the start of each instruction execution
A fixed frequency clock will be used to increment this counter
How will the IS know how many steps there are for this instruction? tbd
  Could have one data bit of each ROM word to mean “end of sequence” or
  Could have the first ROM word in the sequence contain the number of steps

## Slide 7
IS (Instruction sequencer) Page 6: ROM Examples – Common for all opcodes
Let’s assume, for all examples, that:
The PC is adjusted at the end of each instruction so ...
  At at the start of each instruction the PC contains the correct value for fetching the next instruction, and the code ROM output is ready to read.
That dedicated hardware (not control ROM contents) will be used to read the instruction ROM output into the IS block.
So the control ROM is used after the IS has worked out the value to put in the “instruction number” bits of the control ROM address.
  TBD maybe the op code can have bits for “instruction number”?
  In general there must be some kind of design interaction between values chosen for the opcode bits and the instruction sequencing hardware.

## Slide 8
IS (Instruction sequencer) Page 7: ROM Examples – And Ra,Rb - Sequence
First define the sequence of steps required for this specific instruction:
Tell Ra to output its value on the data bus
Tell ALA (ALU Input A) to store the value from the data bus
Tell Ra to stop outputting on data bus
Tell Rb to output its value on the data bus
Tell ALB (ALU Input B) to store the value from the data bus
Tell Rb to stop outputting its value on the data bus
Tell ALU what operation to perform tbd:
  Perhaps this could be step 1
  Does IS output this information on control lines? (I assume so)
  Hence it doesn’t output this via the data bus
Tell ALU output to put the result on the data bus
Tell Ra to store the value from the data bus
Tell ALU to stop outptting its value on the data bus
Increment PC

## Slide 9
IS (Instruction sequencer) Page 8: ROM Examples – And Ra,Rb – Control ROM contents
Assume this is instruction number 4 (no reason, just for example)
A9 | A8 | A7 | A6 | A5 | A4 | A3 | A2 | A1 | A0 | ROM Data
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | Signal to enable Ra output on data bus (note 1)
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | Signal to tell ALA to store the value from the data bus
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | Signal to disable Ra output from data bus (note 1)
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | Signal to enable Rb output on data bus (note 1)
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | Signal to tell ALB to store the value from the data bus
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | Signal to disable Rb output from data bus (note 1)
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | Signals to tell ALU what operation to perform
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | Signal to tell ALU to put output on data bus
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | Signal to tell Ra to store value from the data bus (note 1)
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | Signal to disable ALU output on data bus
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | Signal to increment PC
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | Signal indicating end of instruction sequence
Note 1. The register selection demultiplexer will use the Ra and Rb values from the opcode
The ROM data just needs 1 bit to say “use Ra” and another bit to say “use Rb”.
I’ve not shown exactly how bits in the ROM data are used. I’m mostly trying to explain how using a ROM to control the sequence to execute an instruction can work.
NB: All digital chips (74xx, ROM, RAM) have a resoponse time. So e.g. At the instant an ALU input latch is told to store the value from the data bus, that value may not yet be available at the latch output. Hence why we can do e.g. “enable output” and “store input”
in one step. Tbd, depends on exact details of hardware. Might be able to do this in some cases